## Slide 1
Battery On 3 Out & Up
Steps are Stowed
Silver key - All strapped in
Item 5 complete
2 pushed with 2 pins
Good Price check__over__
CB’s in - center and left
3 outboard
Rudder trim - neutral
Throttles - off
Speed brake center and aft
Compass Mag
Fuel shutoff - up&guarded
Alt gear handle - stowed
Landing lights - off
Handle down 3 green
710 1.2 - 1.4 Bug Set @___
Uncaged & adjusted 3°NL
3 on one __:__ good sweep
Normal Tacan Good Bcn
2 forward Antennae Auto
Both Preset Squelch CH 1
99X T/R ON 109.3 (108.7)
Mag Compass checks good
Altimeter __.__ reads ___
VVI = 0
Enviros Set
Boost Pumps On
Crossfeed off
Generators on
IFF standby
“Ready for my lights”
Light in the handle Horn
3 green 4 fire lights AOA
Master Caution Canopy
Full Panel
Interior Lights Set
Form Lights off
Rotating beacon on
Position lights off
Pubs AOA and Loose
items Stowed
Mask up Visor down
Starting Engines
No O2 or refueling w/i 50ft
Clear fore sides aft& inlets
“Hands Clear” (Connect)
Ready Ready HACK
Off flag out of view
Fuel flow EGT Oil Hydral
Caution Panel Clear Right
“Hands Clear” (Switch)
Ready Ready HACK
Off flag out of view
Fuel flow EGT Oil Hydral
Caution Panel Clear Left
Engage Disengage Re-engage
(Disconnect)
CB’s in Center and Left
Battery On
BEFORE TAXI
Defog, Temp, P. Heat
Yam Damper - on
G-suit zip good squeeze
“Feet and Knees Clear”
Trim checks
Flt. controls - check
Speed brake - check
Flap Slab - check
Flt Dir/COM/NAV chk
3° Nose Low on 2
Heading ____ on 2
Altimeter set __.__
reads ___ w/drop of _ __
IFF checks good
Fuel’s __ good balance
Light at a Liter
X-over good
Seat height adjusted
2 showed and stowed
Good brakes
“Hands Clear”(Chocks)
TAXI/BEFORE T/O
Taxi Lights On
3° Nose Low on 2
(HDG) on 2
Handle down 3 green
Flaps 60
Hyd Oil & Fuel - good
Pins are out
Min-accel is ____
Adj Refusal is ___
Refusal is ____
SETOS is ____
SETOS+10 is ___
Battery’s on
Enviros set
Loose items stowed
Visors down
T/O trim in the green
“Feet and Knees clear”
Flight controls check
Canopies Up w/a light
N - Navaids
E- Emergency Return
W - Weather
S - SID
LINEUP/TAKEOFF
Lights Squawk
Pitot Enviro
Nose Wheel Centered
MIL on the brakes
Engine instr. Check
Clear Telelight Panel
Brake Release - MAX
Centerline Needle off
100 knots taking a tire
Min-accel We’re a go
CLIMB
Hot and Dry
Oxygen
Fuel
Cabin Alt.
DESCENT
Visor - down
HDG + Attitude
Altimeter - check
Fuel - BUG SPEED
X-feed - off
Defog + temp - set
Pitot/Anti ice - A/R
Land/Pos Lts - On
AFTER LAND
2 Pins - in
Pitot heat - off
Loose items - stowed
Cabin Alt. - check
Ram Dump
Canopies - open
Gear doors - open
T/O trim in the green
Flaps - up
Speed brake - aft
Ldg/Pos lits - off
Center Console - off
IFF - off
Cabin press - on
SHUTDOWN
Eng 70% - 1 min
Seats - full up
Pos/form lts - off
Oxygen - 100%
Throttles - off
Beacon - off
Stdby ADI - caged
Ung switches - off
Silver key - secure
Battery - off
Flt. Dir - off
Fuel Norm NF
3500 180 195
3400 179 194
3300 178 193
3200 177 192
3100 176 191
3000 175 190
2900 174 189
2800 173 188
2700 172 187
2600 171 186
2500 170 185
2400 169 184
2300 168 183
2200 167 182
2100 166 181
2000 165 180
1900 164 179
1800 163 178
1700 162 177
1600 161 176
1500 160 175
1400 159 174
1300 158 173
1200 157 172
1100 156 171
1000 155 170
LEVEL OFF
Oxygen
Fuel
Cabin Alt.
Altimeter
T - Time
T - Turn
T - Throttles
T - Twist
T - Track
T - Talk
W - Weather
H - Holding
O - Obtain Clearance
L - Letdown Plate
D - Descent check
S - Speed
N - Navaids
M - Minimums
A - Altimeter
I - Initial rate descent
L - Lost comm
M - Missed approach
A - Airspeeds
N - Next approach
L - Localizer
I - Inbound Course
D - DME
S - Speed